## Slide 1
RTL deep dive
Academic viva
DW module
Depthwise wrapper plus shared compute core
How the depthwise path streams pixels, creates 3x3 windows, accumulates MACs, and only finishes when the last AXI output beat is accepted.
RTL anchors: dw_plane_run_axis.sv, compute_engine.sv, line_buffer.sv, conv_mac_array.sv, ppu.sv
Cover thesis
dw_plane_run_axis is the shell that makes the accelerator behave like a stream endpoint. The real arithmetic path is inside compute_engine, which this shell locks into depthwise mode.
Presentation promise
We will follow one pixel from AXI ingress to AXI egress, showing exactly where buffering, window legality, MAC validity, quantization, TLAST, and external completion are decided.

## Slide 2
DW datapath in one glance
The wrapper owns stream adaptation and output accounting. The core owns padded window generation, convolution, and post-processing.
shell / core split
AXI input
MM2S byte stream
s_axis_tvalid / tready
->
Input FIFO
Decouples DMA from real pixel consumption
->
line_buffer
Pads internally and emits valid 3x3 windows
->
conv_mac_array
9 signed products plus adder tree
->
ppu
Bias, requantize, clamp, optional ReLU
->
Output FIFO
Stores {tlast,data}
and absorbs backpressure
->
AXI output
S2MM stream
m_axis_tvalid / tready / tlast
Wrapper region: dw_plane_run_axis
Shared compute_engine configured for depthwise mode
Wrapper decisions
s_axis_tready goes low when the input FIFO is full or start_in is flushing state.
throttle_in halts core intake when the output FIFO approaches full.
m_axis_tlast is stored per output pixel, not computed on the fly at the port.
Core configuration for DW
is_depthwise = 1
bypass_1x1 = 0
mode_residual = 0
psum_clear = 1 and residual inputs are tied off
What the audience should remember
The shell guarantees correct stream behavior.
The core guarantees correct math over a virtual padded image.
The two are coupled by FIFO contracts rather than direct AXI timing.
Slide claim verified against dw_plane_run_axis.sv and compute_engine.sv.

## Slide 3
What dw_plane_run_axis actually owns
It is the stream shell around a shared compute engine: parameter capture, FIFO decoupling, output counting, TLAST tagging, and external completion.
top-level contract
Control
start_in, done_out
Geometry
img_width, img_height, pad_top, stride_2
Quantization
zp_in, zp_out, bias_in, mult_in, shift_in
Kernel
weights_3x3[2:0][2:0]
Ingress AXI
s_axis_tdata / tvalid / tready / tlast
Egress AXI
m_axis_tdata / tvalid / tready / tlast
Wrapper-specific control logic
- Derived out_w / out_h determine how many pixels must be emitted.
- produced_cnt marks the last generated pixel before it enters the output FIFO.
- done_out does not follow core_done; it waits for final AXI acceptance.
Input side behavior
- s_axis_tready = !in_full && !start_in
- Input FIFO uses show-ahead read: pixel_in always sees in_mem[in_rd_ptr].
- in_pop happens only when consume_in && valid_in, so padding does not advance the FIFO.
Output side behavior
- Each output FIFO entry stores {last, data} as a 9-bit word.
- throttle_in rises when out_count >= OUT_FIFO_DEPTH - 32.
- done_out = m_axis_tvalid && m_axis_tready && m_axis_tlast.
One subtle but important note
The wrapper contains an explicit comment that its stride-2 output size formula is a ceil(W/2), ceil(H/2) approximation for the network being targeted. That is acceptable for the current use case, but it is still a model-level assumption worth stating in a viva.
Presentation takeaway: the shell is not mathematically deep, but it decides what the outside world believes the accelerator has completed.
Verified against dw_plane_run_axis.sv: FIFO control, output counting, TLAST generation, and top-level done_out.

## Slide 4
line_buffer turns a 1D stream into a padded 3x3 view
Padding is synthesized internally with zp_in, so the input FIFO only advances when a real source pixel is needed.
window generator
Internal storage structure
line1 BRAM
Two rows back at the current column tap
line0 BRAM
Previous row at the current column tap
Shift registers
s0_x, s1_x, s2_x hold the current 3-column neighborhood
How a window is formed on each advance
s0_0
s0_1
s0_2
s1_0
s1_1
s1_2
s2_0
s2_1
s2_2
At every advance: s2_2 gets px_gen, s1_2 gets line0[gen_col], and s0_2 gets line1[gen_col]. Then line0 stores px_gen and line1 stores the old line0 value.
Key predicates
need_real_px: current generated coordinate lies inside the real image bounds
advance: running && (!need_real_px || valid_in)
consume_in: advance && need_real_px
What that means architecturally
Padding cells do not consume FIFO bytes.
Real cells stall until valid_in is present.
The line buffer owns the exact pacing contract for the core.
When does lb_valid_out rise?
Only after enough state exists to define a legal output center.
For stride_2, output_valid_check keeps only even center_r / center_c locations.
For this DW wrapper, bypass_1x1 is 0, so the full 3x3 path is always used.
Internal done signal
line_buffer done_out pulses when the final padded coordinate is processed.
That is a core-completion event, not the same thing as the wrapper's stream completion.
Verified against line_buffer.sv: padded virtual image generation, consume_in semantics, output_valid_check, and line RAM update order.

## Slide 5
conv_mac_array performs the actual depthwise convolution
For DW mode the block uses all nine taps, subtracts zp_in per activation, and ignores psum_in entirely.
2-stage MAC
Depthwise datapath equation
mac_out = sum over 3x3 [ (window[r][c] - zp_in) * weights[r][c] ]
The pointwise accumulation path exists in the shared module, but the DW wrapper forces is_depthwise = 1 and psum_clear = 1, so the partial-sum path is logically bypassed.
(w00 - zp) * k00
(w01 - zp) * k01
(w02 - zp) * k02
(w10 - zp) * k10
(w11 - zp) * k11
(w12 - zp) * k12
(w20 - zp) * k20
(w21 - zp) * k21
(w22 - zp) * k22
Stage 1: registered products
Nine signed 18-bit product registers p00_r ... p22_r are captured in always_ff.
This maps naturally onto DSP multiply registers rather than leaving all products combinational.
valid_s1, is_dw_s1, psum_clear_s1, and psum_in_s1 pipeline the control alongside the data.
Stage 2: balanced adder tree
Products are grouped into s0 ... s4 and then reduced into tree_sum.
For DW, mac_next = tree_sum.
For non-DW, only p11_r is used and psum_in can be accumulated.
Pipeline meaning
lb_valid_out marks a valid 3x3 window.
mac_valid_out appears after the product-register stage and output-register stage have done their work.
The design is throughput-oriented: once windows arrive regularly, a new MAC result can emerge every cycle.
Verified against conv_mac_array.sv: depthwise tap selection, registered products, balanced adder tree, and psum handling.

## Slide 6
PPU converts accumulator output back to 8-bit pixels
In the DW wrapper the residual path is disabled, but the shared PPU still carries both conv and residual machinery.
4-stage post-processing
Stage 1
acc + bias, then multiply by mult_conv
Stage 2
absolute value, sign extraction, path selection
Stage 3
right shift with ties-to-even rounding, sign restore, zp_out add
Stage 4
clamp to [0,255], then optional ReLU floor at zp_out
Quantization equation, conceptually
q = RoundTiesToEven( (conv_acc_in + bias_in) * mult_conv >> shift_conv ) + zp_out
The hardware separates sign handling from magnitude handling. Stage 2 forms an absolute-value path, stage 3 performs the barrel shift and rounding on magnitude, then the sign is restored before zero-point addition.
That split matters because the 68-bit negate and shift logic is one of the architectural hotspots in the local timing analysis.
Residual path status in DW mode
mode_residual = 0 in the DW wrapper.
res_a_in, res_b_in, mult_res_a, mult_res_b, shift_res, zp_in_a, and zp_in_b are tied off.
So ppu_trigger follows mac_valid_out, not raw valid_in.
ReLU status
relu_en = 0 in dw_plane_run_axis.
The ReLU hardware still exists in the shared PPU, but it is inactive for this DW shell instance.
Output contract
PPU valid_out only means a quantized pixel exists for the wrapper.
The wrapper still has to store it, tag tlast, and wait for AXI acceptance.
Verified against ppu.sv: 4-stage conv path, ties-to-even rounding, zero-point add, clamp, and ReLU gating.

## Slide 7
Control timing: valid is not the same as done
The most defensible way to explain control is to follow one real pixel through the contracts that transform it into one accepted output beat.
handshake semantics
1. in_push
s_axis_tvalid && s_axis_tready
writes FIFO
2. valid_in
FIFO non-empty and not throttled
3. consume_in
line_buffer needs a real pixel now
4. lb_valid_out
A legal 3x3 center exists
5. mac_valid_out
The MAC pipeline has finished this window
6. valid_out
PPU has produced an 8-bit pixel
7. out_push
Wrapper stores {tlast,data}
8. done_out
Final beat is accepted on AXI output
Why consume_in matters
consume_in is the only signal that proves a source byte was truly consumed by the core.
Padding positions self-generate zp_in and therefore do not pop the input FIFO.
Why valid_out is not enough
PPU valid_out only means the wrapper may push the output FIFO.
If the DMA sink stalls, the final pixel can exist internally long before external completion is visible.
Why wrapper done_out is strong
done_out = m_axis_tvalid && m_axis_tready && m_axis_tlast
That definition means the module reports completion only after the outside world has actually accepted the last pixel.
Verified against dw_plane_run_axis.sv, compute_engine.sv, and line_buffer.sv: in_push, valid_in, consume_in, valid_out chain, TLAST tagging, and done_out semantics.

## Slide 8
Design critique and viva defense points
This slide turns the RTL into an engineering argument: what is already sound, where the bottlenecks are, and what tradeoffs the current implementation has accepted.
viva critique
32 entries
Throttle margin before output FIFO saturation
Core done != stream done
line_buffer completion is intentionally weaker than wrapper completion
~40-65 MHz
Local estimate for current bottlenecked Fmax from existing analysis notes
Strengths worth defending
Clear shell/core separation keeps stream semantics outside the arithmetic core.
consume_in cleanly distinguishes padding from real pixel fetches.
Top-level done_out is externally meaningful because it is acceptance-based.
Known limitations
The wrapper comment explicitly admits an approximate stride-2 output-size rule for the current network assumptions.
The compute_engine instance produces an internal core_done that the wrapper does not expose.
Throughput is likely limited by the PPU post-processing path rather than the wrapper FIFOs.
Natural improvement path
Pipeline the PPU further if timing becomes the dominant issue.
Parameterize image-width limits instead of hard-wiring 2048 in line_buffer.
If the system grows, make the wrapper's size formula exact and document the supported convolution cases.
Critique points grounded in dw_plane_run_axis.sv and the existing compute_engine_analysis.md timing report.